|  | 10/14/2008 |
| --- | --- |
|  | Bilkent University Team 6 Özgün ÇITLAK Çiğdem ARDAHAN Kıraç SÖĞÜTLÜ Arda KART Altuğ ZAİMOĞLU Ege GÖRGÜLÜ |

[Product definition Document] Project Name: vtravel - Travel help for visually impaired people

The document contains the description of the product and its features.

Table of Contents

1.	General Product Information	3

1.1.	Functions	3

1.2.	Interface	4

1.3.	Physical Characteristics	5

1.4.	Power Supply	5

1.5.	Environmental Characteristics	6

1.6.	Standards Complied With	6

2.	Nokia N810 Internet Tablet	7

2.1.	Features	7

2.2.	Images	9

3.	Braille Keyboard for Nokia Tablet	10

3.1.	Features	10

4.	Jabra BT2010 Headset	10

4.1.	Features	10

5.	Navigation System	11

5.1.	Features	11

5.2.	User Interface	11

6.	References	13

# General Product Information

The aim of the product is to help visually-impaired people increase their ability to find their directions. In addition to this, the system will give the visually-impaired people the opportunity to do things without the help of others. Even though the system is designed primarily for the visually-impaired people; since we will also use visual components to show the data, the people with “hard of hearing” can also benefit from the product.

Below are some key components explained in detail in the following sections:

- Nokia N800 Internet Tablet with integrated GPS receiver,

- A keyboard that supports Braille alphabet,

- An headset that connects to the system via Bluetooth,

- Visual and auditory navigation system,

In the subsections below, firstly, the set of features that are common throughout the parts of the project are explained. Then information about the interface, physical characteristics, power supply, environmental characteristics and the standards it complies with is given. In order to learn about features of the specific components of the product, further read the document.

## Functions

- The voice will be clear and be easily heard even at crowded and noisy places.

- Automatically detects the current location of the user,

- Automatically recalculates the directions if the user misses a turning point and alerts the user about the changes,

- Reads out loud the menus and one-sentence usage of them,

- Shows the current location of the user on the map and updates his position on the map as he travels along the route,

- Displays, and speaks out, the distance in meters, in number of blocks and in personal footsteps, and automatically updates the numbers during travel,

- Displays, and speaks out, the estimated time to arrive at the destination,

- Designed for 24 months of lifetime.

## Interface

- Bluetooth 2.0:

This technology allows easily connecting the headset with Nokia Tablet.

- Have an embedded Braille keyboard:

This keyboard is the main input device, which is specially designed for visually impaired people.

- Have an LCD touch screen keyboard:

This keyboard can be used as an input device for people who do not have a loss of sight.

- Keyboard language supports multiple languages.

English, German, French, Italian, Spanish-Portuguese, Scandinavian and Russian are supported. Turkish language can be used without Turkish-specific letters ç, ö, ğ, ü, ş, ı changed into corresponding letters c, o, g, u, s, i.

- The Navigation software we write supports Turkish language.

The narrator that tells the directions for a route will talk in Turkish and the explanations on the screen will be in Turkish.

- The user interface is summarized below. To learn about details of the user interface, refer to “Section 5.2. User Interface”.

  - The user menu will have the following options:

    - “Where Am I?”: 	If selected, this option will show the user’s current location on the map. For visually impaired people it will announce the current place.

    - “Plan a Trip”:	If selected, this option calculates the directions to go to the given destination which is inputted from the keyboard (touch screen or Braille keyboard). For visually impaired people, this option also speaks out the directions as the user requests or automatically within some time intervals depending on the configuration.

    - “Settings”: 		If selected, this option allows the user to configure the settings for “Voice”, “Display” and “Auto-Update”.

    - “Exit”: 	If selected, this option allows the user to close the application and return to main menu.

  - The user will be able to exit from the application at any time.

  - The user will be able to go back to the previous menu at any time.

## Physical Characteristics

- Dimensions (Length x Width x Height):

For Nokia Tablet: 2.83 x 5.04 x 0.55 in (71.9 x 128.0 x 13.9 mm)

For Headset: 22.5 x 43.5 x 10 mm

- Weight:

For Nokia Tablet: 7.97 ounces (225.95 grams)

For Headset: 11 grams

- Has a modern and good looking design.

## Power Supply

- Nokia Tablet uses rechargeable batteries.

The batteries are BP-4L rechargeable batteries and they can be recharged using AC-4 travel charger that comes with the product.

- Headset uses locked rechargeable batteries that can be recharged with its adapter.

- Battery life:

For Nokia Tablet: Up to 4 hours of continuous usage with wireless LAN on; up to 10 hours of music playback (Wi-Fi turned off); up to 14 days on standby.

For Headset: Up to 8 hours with Bluetooth on, and up to 200 hours on standby.

## Environmental Characteristics

- User can use the product under rain and snow:

The Nokia tablet can be kept in a case and its speakers should be enabled to use without headset. Or, the headset can be used with the head covered with some protective material that keeps the rain out.

- The display of Nokia Tablet is expected to work well even under direct sunlight; however, some feedback says that the display is washed out a bit.

## Standards Complied With

- WLAN standards: IEEE 802.11b/g standards

- Bluetooth specifications v2.0 + EDR (profiles supported: HID, FTP, DUN, GAP, SPP, HSP, SAP and OPP)

- Waste of Electrical and Electronic Equipment (WEEE) directive requirement for recycling:

The product is marked according to WEEE directive requirement for recycling and should not be disposed as unsorted municipal waste.

- ISO 11469 and ISO 1043-1 to -4 standards:

The parts of the product have been marked where practically possible3. Plastic parts are marked in accordance with ISO 11469 and ISO 1043-1 to -4 standards.

- EU RoHS Directive 2002/95/EC:

The product does not contain cadmium, mercury, lead, chromium VI+, Polybrominated Biphenyls (PBB) and Polybrominated Diphenyl Ethers (PBDE), in accordance to EU RoHS Directive 2002/95/EC.

- Energy Star standards:

The power supply for Nokia Tablet is qualified by Energy Star.

# Nokia N810 Internet Tablet

This device is the most crucial component for the product. The application we will implement will run on Nokia N810 Internet Tablet and enable the users to navigate around freely.

## Features

- Weight: 7.97 ounces (225.95 grams)

- Size (Length x Width x Height): 2.83 x 5.04 x 0.55 in (71.9 x 128.0 x 13.9 mm)

- RAM: 256.00 MB,  DDR SDRAM

- Web 2.0 internet experience with Mozilla based browser, also works with Skype, Google Talk, and Gizmo

- Stream and store MP3s and videos with high quality stereo sound

- 2 GB onboard memory, which expands via Secure Digital, SDHC, MMC, miniSD, and microSD cards (with extender)

- 4.1-inch LCD wide touch-screen and full QWERTY keyboard:

The 4.1-inch touch screen has an 800 x 400-pixel resolution with up to 65K colors. You can access controls and an onscreen keyboard, or slide-out the physical QWERTY keyboard at the bottom for even easier typing.

- Integrated GPS receiver:

Perfect for use on the go, the N810 includes an integrated GPS receiver and comes with preloaded maps that enable you to browse detailed locations, search for street addresses, find various points of interest (POI) as well as nearby Wi-Fi hotspots.

- Battery life:

Up to 4 hours of continuous usage with wireless LAN on

Up to 10 hours of music playback (Wi-Fi turned off)

Up to 5 days while always online

Up to 14 days on standby

- Processor:

The Nokia N810 has a 400 MHz Texas Instruments OMAP 2420 processor.

- Operating System: OS2008

The Nokia N810 is powered by maemo Linux-based OS2008, which offers a highly customizable user interface and contains various features such as a Mozilla based browser with Ajax, Adobe Flash 9 and RSS feed reader, Bluetooth headset support as well as enhanced video and audio features.

- Wi-Fi: 802.11b/g:

The main form of connectivity is Wi-Fi (802.11b/g), and hooking up to a network is as simple as connecting with a laptop.

- Bluetooth: Version 2.0 + EDR (profiles supported: HID, FTP, DUN, GAP, SPP, HSP, SAP and OPP) :

You can also use the integrated Bluetooth wireless connectivity to hook up with a cell phone that is compatible with online data services.

- The N810 has two integrated speakers as well as a 3.5mm headphone jack for personal listening.

## Images

Below are several images of Nokia Internet Tablet.

Figure 1 – The 4.1 inch LCD display

Figure 2 – The keyboard that slides out.

# Braille Keyboard for Nokia Tablet

This keyboard will be produced exclusively for the product and it will enable visually impaired people to use the keyboard more efficiently. Since the letters and numbers will be still visible, it will not affect the way it is used by other people. This keyboard will be replaced with the keyboard that comes with Nokia Tablet.

## Features

- Full QWERTY keyboard:

- Supports standard Braille alphabet:

The keyboard will have raised letters that correspond to letters in a standard QWERTY keyboard. Turkish-specific characters (ç, ö, ğ, ü, ş, ı) are ignored and alternative letters (c, o, g, u, s, i; respectively) should be used instead.

# Jabra BT2010 Headset

This headset enables the people to hear on one ear and keep the other ear free. It connects to the Nokia Tablet using Bluetooth connection.

## Features

- Weight: 11 grams

- Size (Length x Width x Height): 22.5 x 43.5 x 10 mm

- Connect wirelessly while on-the-go

- Use your headset for up to 8 hours without recharging.

- Has a capacity of 200 hours standby.

- Size your headset with the adjustable and optional ear hook.

- Operating range: 10m

- Operating keys: Mute and adjusting volume

- High quality of sound

- Latest Bluetooth technology: Includes EDR & Esco Bluetooth 2.0.

# Navigation System

This software is the main focus of our company and it is the essential part of the product. This application we will implement will run on Nokia N810 Internet Tablet and enable the users to navigate around freely.

## Features

- Menus can be listened crystal clear as well as they look good,

- Step by step directions for your trip from Microsoft Virtual Earth,

- Hear and see how many footsteps (or blocks or meters) you are away from your destination,

- Learn estimated time to arrive at the destination,

- Allows changing some of the important settings such as voice and display controls.

## User Interface

The user interface is explained below:

- The main menu that will be on the screen as the application starts first time will have the following three options:

  - “Where am I?” –   If this menu is selected (by pressing letter “W”), the current location of the user will be shown on a map. The location is also going to be read out loud for visually impaired people.

  - “Plan a Trip” – 	If this menu is selected (by pressing letter “P”), it will prompt the user for a destination address. This request will be read out loud for visually impaired people. After receiving the destination via keyboard (which can be touch screen keyboard or Braille keyboard), the directions will be received using Microsoft Virtual Earth. These results then are told to the user, starting from the first step. On the screen the map with the current location of the user marked will be shown and the information about the total distance (in meters, number of blocks and footsteps) will be printed on screen. All these information will be available as audio for visually impaired people.

  - “Settings” –  This menu item if selected (by pressing letter “S”), will  present the user the option to change the configurations of the following components:

    - “Voice”: 	The options available under this component are “Mute”, “Increase”, “Decrease” and “Gender (Male or Female voice)”. Using these options the users will be able to change the volume level and the voice type the narrator speaks.

    - “Display”:	The options available under this component are “Show/Remove Map”, “Show/Remove Full Directions”, and “Distance Units”.  Using these options users will be able to view and ignore maps and directions. They will also have an option to select which units they want to see the distance in: meters, blocks and/or footsteps.

    - “Auto-Update”:	This will set the time interval at which the location and the route will be automatically recalculated. The available options will be “Off”, “5 sec”, “15 sec”, “30 sec”, “1 min” and “5 min”.

  - “Exit” – If this option is selected (by pressing “shift + E”), then the user will exit the application.

- While the application is running the user will be able to exit the application by pressing “shift + E” at any time.

- While the application is running the user will be able to return back to the previous menu, if any available, by pressing “shift + B” at any time.

# References

- Nokia N-series Website.

< http://www.nseries.com/index.html#l=products,n810 >

- Nokia’s Howto Website.

< http://www.nokiahowto.com/A4626059 >

- Nokia Eco-Declaration for N810.

< http://nds1.nokia.com/eco_declaration/files/eco_declaration_phones/N810_Eco-declaration.pdf >

- Wikipedia website.

<http://en.wikipedia.org/wiki/GPS_for_the_visually_impaired>